## Slide 1: Recieve List Error Model

## Slide 2: Error Model
Error models simulate link level errors or losses.
Types:
Stochastic Models
Deterministic/Empirical models

## Slide 3: Receive List Error Model
It is an empirical error model
When it is provided a list to corrupt the model induces errors in particular packets based. The errors follow a pattern and if the pattern is found on the receiver’s end then the packet is declared errored
This model also processes user generated list of packets but the packets to be errored are not selected by packed UID

## Slide 4: Out Pattern
Let us pass a string say “Surathkal”
The binary string array containing 8-bit binary string of ASCII values of each character is as follows:
[01010011, 01110101, 01110010, 01100001, 01110100, 01101000, 01101011, 01100001, 01101100]

## Slide 5: Our Pattern….
Each of these strings are converted to 16-bit strings by doing exclusive-Or of one bit with its neighbouring bits and also of first and last bits. The resulting array is as follows:
[0101001111110101, 0111010110011111, 0111001010010110, 0110000110100011, 0111010010011100, 0110100010111000, 0110101110111101, 0110000110100011, 0110110010110100]

## Slide 6: Our Pattern...
The generated pattern is then induced with an error pattern.
We decided to change all the alternate bits of the string.
The strings to be errored are randomly selected and the frequency of the error is decided according to the error rate. Error rate is between 0 and 1.

## Slide 7: Our Pattern...
In our example the error rate is taken to be 0.3 . The string array generated is:
[0101001111110101, 0111010110011111, 1101100000111100, 0110000110100011, 0111010010011100, 0110100010111000, 1100000100010111, 0110000110100011, 0110110010110100]
Now the string is passed to the receiver’s side and the bits are exclusively-ORed with their neighbouring bits and the output is checked with the corresponding bits in the string. This way pattern is detected.
The received string is “SuXathAal”. There are two errors in the received string ‘X’ instead of ‘r’ and ‘A’ instead of ‘k’ is received.

## Slide 8: Simulation
We have used single simulation file that loops three nodes, all initialized with same location value(origin).
OneShotBehavior is used to create a Behaviour for sending and receiving of the string between nodes
Use of TxFrameReq and ReceiveFrameNtf (instance)

## Slide 9: Simulation ...
At Node1: Input is taken as a string, and it is transmitted to node 2
At Node2: The received string from node1 is corrupted using ReceiveListErrorModel and the resulting string is passed to node3
At Node3: The received string from node 2 is cross-checked/verified.